## Slide 1: Storage and Stress Packages

## Slide 2: Packages
Internal Packages
  Storage (STO) Package
  Time-Varying Storage (TVS) Package1
  Skeletal Storage, Compaction and Subsidence (CSUB) Package 1
  Horizontal Flow Barrier (HFB) Package1
  Buoyancy (BUY) Package1
  Viscosity (VSC) Package1
1 Will not be covered
Standard Stress Packages
  Constant Head (CHD)
  Recharge (RCH)
  Well (WEL)
  River (RIV)
  Drain (DRN)
  General Head Boundary (GHB)
  Evapotranspiration (EVT)
Advanced Stress Packages2
2 Will be covered later

## Slide 3: Storage (STO) Packages
Steady state if STO Package not specified for a simulation
Aquifer storage properties are specified
Individual stress periods are marked as steady state or transient

## Slide 4: STO Input File

## Slide 5: STO Input File
ICONVERT=0: cell is treated as confined for storage calculations
ICONVERT=1: cell converts between confined and unconfined depending on head

## Slide 6: STO Input File

## Slide 7: STO Input File
Stress periods can be marked as “STEADY-STATE” or “TRANSIENT”

## Slide 8: Recharge package

## Slide 9: Recharge Definition
Precipitation
Evapotranspiration
Runoff
Recharge
Recharge = Precipitation – Runoff – Evapotranspiration

## Slide 10: Recharge Formulation
QR = I x A
  I is recharge rate (L/T) entered by user
  A is the cell area
Negative values indicate discharge
Applied directly to a cell – percolation time through the unsaturated zone is not represented
RHS = -QR
Only complication is deciding which cells receive recharge

## Slide 11: Apply Recharge to Highest Active Layers (default)
Recharge applied to cells with an X

## Slide 12: Apply Recharge to Top Layer
Recharge applied to cells with an X

## Slide 13: Apply Recharge to Specified Layers
Recharge applied to cells with an X

## Slide 14: Recharge Package Example
List-based input
Array-based input

## Slide 15: Well package

## Slide 16: Well Package
Q = User-specified Q
Use consistent units (L3/T)
Negative values indicate discharge
Positive values indicate injection
RHS = -Q
AUTO_FLOW_REDUCE can be used to turn wells off as head in cell approaches cell bottom

## Slide 17: Well Package Input

## Slide 18: River package

## Slide 19: River Package
Simulates the impact of rivers on the aquifer – not the river itself

## Slide 20: River Package – Conceptual Model

## Slide 21: River Package – Conceptual Model

## Slide 22: River Package – Conductance Conceptualization
Riverbed conductance = KLW/b

## Slide 23: River Package – Aquifer/River Connection
QRIV = CRIV(HRIV – hcell)
If hcell > RBOT
QRIV = CRIV(HRIV – RBOT)
If hcell <= RBOT

## Slide 24: River Package – Head-Dependent Flow

## Slide 25: River Package – Discretization Issues
The river equation is a simplification
Each reach is independent of the other reaches
Things to consider:
  Are there multiple reaches in cell?
  What is the length of a reach in cell?
  What is the appropriate river head for a reach?
  Are multiple reaches needed or can a composite/average river cell be used?
If a preprocessor is used, how does it define a river cell?

## Slide 26: River Package Example

## Slide 27: Drain package

## Slide 28: Drain Package

## Slide 29: Drain Package – Head-Dependent Flow

## Slide 30: Drain Package Example

## Slide 31: General-head boundary package

## Slide 32: General-Head Boundary Package
QGHB = CGHB (HGHB – hcell)

## Slide 33: General Head Boundary – Head-Dependent Flow

## Slide 34: General Head Boundary Example

## Slide 35: Evapotranspiration package

## Slide 36: Evapotranspiration Package

## Slide 37: Evapotranspiration Package Example
List-based input
Array-based input

## Slide 38: Comparison of stress packages